## Slide 1
>> IN THE NAME OF ALLAH, THE MOST GRACIOUS, THE MOST MERCIFUL <<
SENSITIVITY ANALYSIS OF SOIL DAMPING RATIO, YIELD STRENGTH, ELASTIC STIFFNESS, DUCTILITY RATIO AND OVER-STRENGTH FACTOR ON THE SEISMIC PERFORMANCE OF SOIL–STRUCTURE MDOF SYSTEMS USING OPENSEES: CYCLIC DISPLACEMENT AND SEISMIC TIME-HISTORY ANALYSES WITH EVALUATION OF PERIOD ELONGATION,ENERGY DISSIPATION CAPACITY INDEX, EQUIVALENT VISCOUS DAMPING RATIO, DUCTILITY DAMAGE INDEX AND RECONSTRUCTION COST
THIS PYTHON SCRIPT IS WRITTEN BY SALAR DELAVAR GHASHGHAEI (QASHQAI)

## Slide 3
This OpenSeesPy-based Python framework performs a comprehensive multi-parameter
sensitivity analysis of a two-degree-of-freedom nonlinear soil–structure system subjected
to both cyclic displacement protocols and selected ground-motion time histories.
By systematically varying soil yield strength, elastic stiffness, ductility ratio,
over-strength factor, and viscous damping ratios of both soil and structure across a
discrete design space, the code assembles a high-fidelity hysteretic model using multi-linear
OpenSees hysteretic materials and parallel viscous dampers, extracts instantaneous eigenvalue
periods at every analysis step to quantify period elongation, and computes a suite of performance
metrics including peak displacement, velocity and acceleration demands, energy-dissipation capacity
index, equivalent viscous damping ratio from hysteresis loops, ductility-based damage index, and
reconstruction cost. Extensive post-processing then generates correlation scatter plots,
three-dimensional response surfaces, Pearson sensitivity heatmaps, Random-Forest safety
classification, and both main-effect and interaction ANOVA tables, thereby ranking the relative
influence of each soil and structural parameter on seismic performance and providing a rigorous
quantitative basis for performance-based design and risk assessment of soil–structure systems.